## Slide 1
Rapport du Comité de Suivi Individuel
09th / 10 / 2019
Young Jun Kim(1,2), David Le Touzé(1)
(1) Ecole Centrale de Nantes, France, (2) Bureau Veritas, France

## Slide 2: General information
Affiliation
  School : École Centrale de Nantes (ECN)
  Lab : LHEEA
  Team : H2I (Hydrodynamique, Interfaces et Interactions)
Date of admission
  01/01/2018 (1 year 10 months)
Financement
  CIFRE contract from Bureau Veritas (BV) and ECN
Encadrants de thèse
  David Le Touzé (Directeur)
  Benjamin Bouscasse (Co-encadrant)

## Slide 3: Objective
Numerical improvement and validation of a naval hydrodynamics CFD solver in view of performing fast and accurate simulation of complex ship-wave interaction.
Naval applications
Efficiency
Numerical Improvement
One of Petrobras’ FPSOs in Brazil; Source: Petrobras
Higher-order schemes?
Notes: Tentative title
Do numerical improvement
Check its efficiency
Do real naval application with improved sovler.
CFD solver used is:

## Slide 4: What makes the problem complicated?
Two-phase incompressible viscous (Newtonian) flow solver.
  There are many important issues.
  The most critical thing is the interface (discontinuity).
VOF, density, mass flux, dynamic pressure, viscosity
Body
Governing equations
Notes: Why do we need improved solver?
Discontinuous interface : convection of discontinusous properties is wave propagation : free surface piercing body :: it makes the problem complicated.
So, one of my preliminary study focus on the interface treatment schemes.

## Slide 5: Preliminary study: Interface treatment
The interface treatment schemes
  Interface capturing scheme:
  Interface advection scheme:
  Interface boundary condition:
How to define(capture) the free surface.
How to move interface in time.
How to define the physical properties at the interface.
Ref
The interface capturing scheme is VOF.
Periodic wave propagation test
Finer grid
Ref
Notes: Two interface advection scheme
Two interface boundary condition
The plot shows normalized averaged amplitide in period 1-10 respect to grid resolution.
As the grid number increase we have finer mesh.
GFM has numerical damping, Isoadvector have good conservation of wave amplitide but it is little unstable.
The reference solver is not always good, but it shows a predictable results.

## Slide 6: Preliminary study: Waves
Wave generation and absorption.
Increased viscosity & artificial damping source
Explicit Relaxation method is used to generate wave.
Various outlet conditions are studied
Relaxation to incident wave & no wave (calm water).
Mesh streatched outlet
Notes: Another preliminary study is on ...
In foamStar we use explicit relaxation method to generation and absorption waves
To validate this other wave absorption methods are studied.

## Slide 7: Preliminary study: Waves
Wave generation and absorption.
If without body, Indicent wave outlet condition gives most stable and precise wave propagation.
If the condition of outlet is different to the incoming wave, it makes wave reflection and phase shift.
Notes: We have two conclusion.

## Slide 8: Numerical Improvement Higher-order schemes
Higher-order scheme.
Spatial scheme
Temporal scheme
The higher-order schemes are believed to have the advectage on high-order accuracy
Algorithms and its applications are complicated.
The temporal schemes are studied first, beacuse it is more simple.
Notes: I choose higher-order scheme as a numerical improvement.
The higher-order schemes are believed to have the advectage on high-order accuracy.
So I have to do both HO spatial and HO temporal discretization scheme.
Consider a ODE
If mesh do not move, the problem is 1D in time.

## Slide 9: Higher-order temporal schemes
Diagonally Implicit Runge-Kutta (DIRK) method
Only SA DIRKs are used.
Butcher matrix
Singly Diagonally IRK
SDIRK Stiffly accurate
Explicit first SDIRK
ESDIRK SA
ODE
Diagonally implicit
Explicit
Notes: Only SA DIRKs are used bacuase it is more stable.
SA prevent to solve eq(3) which help not to use explicit limiter again in the VOF convection equation.

## Slide 10: Higher-order temporal schemes
Previous RK iteration data must be used.
Thus, each governing equations must change.
Explicit term
Notes: Full algorithm
The RK loop will place upon the PIMPLE loop.
So, this means if i use 2 stage DIRK scheme, the compuational time will be double.
Also, inside the PIMPLE loop each governing equaiton should change a little due to the explicit term.

## Slide 11: Higher-order temporal schemes
RKCN
RK221
RK331
RK334
RK431
Notes: RKCN: 2nd order two stage explicit first scheme
Maximum third order is considered.
The detail stability and order properties will be discuss in the paper.

## Slide 12: Higher-order temporal schemes
Taylor-Green vortex simulation
Analytic solution
vortisity
Vortisity + Streamline
VelocityMag + VelocityVector
Computational conditions
Notes: To validate DIRK scheme simple one-phase TGV simulation is done.

## Slide 13: Higher-order temporal schemes
Taylor-Green vortex simulation
maximum error of velocity magintude
maximum error of pressure
Spatial
Temporal
All spatial schemes are linear
Spatial Convergence of velocity
Spatial error dominant
Temporal error dominant
Notes: The error are measured at t = 2 sec.
The Euler scheme has second order convergence with very course mesh, but the order of convergence decay as the cell size decrease.

## Slide 14: Higher-order temporal schemes
1st
2nd
3rd
Convergence limit due to spatial error
Unstable pressure
Temporal error dominant condition
Convergence limit
Spatial error dominant condition
This can be remedied using off-centering
But lose the convergence order.
The order of convergence is achieved.
Notes: This slide shows the temporal convergence for grid Dx128 and Dx 256

## Slide 15: Higher-order temporal schemes
1st
2nd
3rd
Convergence limit
Notes: So DIRK method seems to be work properly.

## Slide 16: Higher-order temporal schemes
Periodic wave propagation
Reference
Averaged normalized wave amplitude from 1-10 periods
(Computation time) x (nCore)
Notes: Using Periodic wave propagation, we test the DIRK schemes

## Slide 17: Higher-order temporal schemes
Periodic wave propagation
Averaged normalized wave amplitude from 1-10 periods
(Computation time) x (nCore)

## Slide 18: Higher-order temporal schemes
Periodic wave propagation
Black dotted line is reference OFCN095 case
Efficient
Only spatial convergence cases are plotted here to estimate the spatial error.
Height 0.1
Height 0.05
Height 0.01
Grid 1
Grid 2
Grid 3
Grid 4
Notes: It plots the normalized averaged error respect to computational cost.

## Slide 19: Higher-order temporal schemes
Periodic wave propagation
Efficient
The efficient solvers are RKCN and RK221
Higher-order rate of convergences are not observed.
If the wave amplitudes are small, we can use courser mesh

## Slide 20: Higher-order temporal schemes
Periodic wave propagation with moving mesh
DIRK type methods are more efficient then classical OFCN
Error increased compare to the static mesh cases
Imaginary
body

## Slide 21: Higher-order temporal schemes
Near future works
To do a FSI simulation it is good to use SWENSE to control the number of the cells.
1. CALM buoy in regular / irregular wave
2. KCS with waves & forward speed
= incident wave component + complimentary component

## Slide 22: Higher-order spatial schemes
Future works
WENO & WENO reconstruction method.
Stencil 1
Stencil 2
Stencil 3
Need careful formulation
also needs to estimate its efficiency.
Nsi=stencils

## Slide 23
Articles
1. A paper on the higher-order temporal scheme (ongoing).
2. A paper on the interface treatment schemes (Not ready yet).

## Slide 24: Higher-order temporal schemes

## Slide 25: Higher-order temporal schemes

## Slide 26: Higher-order temporal schemes: ALE

## Slide 27: Preliminary study: Waves
Wave generation and absorption.
Increased viscosity & artificial damping source
Explicit Relaxation method (to incident wave & no wave).